## Slide 1
Anticoagulants
Pathology / Hematology — Blood Anticoagulants
Introduction • Mechanism of Coagulation • Properties • Classification • Composition & Ratio • Uses • Blood Bank
Reference: MLT Pathshala — YouTube Channel

## Slide 2
Introduction
Anticoagulants are chemical substances added to blood, in vitro, to prevent it from clotting (coagulating).
They act either by removing/binding calcium ions (Factor IV) from blood, or by directly inhibiting thrombin and other clotting factors.
Blood collected without an anticoagulant clots within a few minutes — the clotted (serum) sample cannot be used for most hematology tests.
Anticoagulated blood is essential for hematological investigations, coagulation studies, and for the safe storage of blood in blood banks.
Different anticoagulants act by different mechanisms and are chosen depending on the test to be performed — no single anticoagulant suits every test.
2

## Slide 3
Purpose & General Uses
Keep blood in a fluid (liquid) state so that it can be examined, processed, or stored.
Enable hematological tests — complete blood count (CBC), hemoglobin, PCV, ESR, blood film examination.
Enable coagulation studies — Prothrombin Time (PT), Activated Partial Thromboplastin Time (APTT).
Provide plasma (instead of serum) for biochemical and immunological assays that require plasma.
Preserve donor blood in blood banks for transfusion, by combining an anticoagulant with a preservative solution.
Used therapeutically (in vivo) to prevent and treat thromboembolic disorders — e.g., heparin, warfarin.
3

## Slide 4
Coagulation Mechanism — Basis of Anticoagulant Action
Normal coagulation proceeds through the Intrinsic, Extrinsic, and Common pathways, ending in the conversion of fibrinogen to fibrin.
Calcium ion (Factor IV) is required at several steps of the cascade — activation of Factors IX, X, and prothrombin to thrombin.
Thrombin converts soluble fibrinogen into insoluble fibrin strands, which trap cells and form the clot.
Anticoagulants interrupt this cascade at one of two points:
  By chelating/precipitating calcium — removing it so the cascade cannot proceed (EDTA, citrate, oxalates).
  By directly inhibiting thrombin/clotting factors — without removing calcium (heparin, warfarin).
4

## Slide 5
Properties of an Ideal Anticoagulant
Should prevent coagulation completely at the correct concentration.
Should not alter the size, shape, or morphology of blood cells.
Should be freely soluble in blood and act rapidly.
Should not interfere with the test to be performed on the sample.
Should be non-toxic, cheap, easily available, and stable on storage.
Should be used in the correct, standardized ratio to blood — excess or deficient anticoagulant both distort results.
5

## Slide 6
Classification of Anticoagulants
A. Calcium Chelating / Precipitating Agents — act by removing or binding calcium (Factor IV):
  EDTA (Ethylenediaminetetraacetic acid) — di/tripotassium or disodium salt
  Sodium Citrate (trisodium citrate)
  Oxalates — Ammonium oxalate, Potassium oxalate, Double (Wintrobe's) oxalate mixture
B. Non-Calcium Chelating Agents — act by directly inhibiting thrombin / clotting factors:
  Heparin — potentiates antithrombin III, inactivates thrombin and Factor Xa
  Warfarin — in vivo, Vitamin K antagonist; inhibits synthesis of Factors II, VII, IX, X in the liver
6

## Slide 7
EDTA (Ethylenediaminetetraacetic Acid)
Composition: Disodium, dipotassium, or tripotassium (K2/K3) salt of EDTA; K2EDTA is the ICSH-recommended form.
Mechanism: Chelates calcium ions, forming a stable, soluble calcium-EDTA complex — calcium becomes unavailable for coagulation.
Ratio/Concentration: 1.2–2.0 mg dry EDTA per mL of blood (lavender/purple-top vacutainer).
Used for: Complete Blood Count (CBC), hemoglobin, PCV, cell counts, and peripheral blood film — the best anticoagulant for preserving cell morphology.
Advantages: Excellent preservation of RBC/WBC morphology; no hemolysis; ideal for hematology automation.
Disadvantages: Unsuitable for coagulation studies or calcium estimation; excess EDTA causes cell shrinkage and can cause EDTA-induced pseudothrombocytopenia (platelet clumping).
7

## Slide 8
Sodium Citrate
Composition: 3.2% or 3.8% aqueous solution of trisodium citrate.
Mechanism: Chelates calcium reversibly, forming soluble calcium citrate — coagulation can be restored by adding back calcium.
Ratio: 1 part anticoagulant : 9 parts blood (1:9) for coagulation tests; 1:4 for the Westergren ESR method.
Used for: Coagulation tests — Prothrombin Time (PT), APTT; ESR (Westergren method); also used as the base anticoagulant in blood bank preservative solutions.
Advantages: Reversible chelation preserves coagulation factors, allowing accurate PT/APTT testing.
Disadvantages: Dilutes the sample (must correct for high/low hematocrit); not suitable for cell counts.
8

## Slide 9
Oxalates (Ammonium, Potassium & Double Oxalate)
Mechanism: Precipitates calcium as insoluble calcium oxalate, removing it from the coagulation cascade.
Ammonium oxalate — causes RBCs to swell; Potassium oxalate — causes RBCs to shrink.
Double oxalate (Wintrobe's mixture): Ammonium oxalate + Potassium oxalate combined in a 3:2 ratio — the opposing effects on cell size cancel out.
Ratio/Concentration: about 2 mg ammonium oxalate + 1.2 mg potassium oxalate per mL of blood (~6 mg mixture/2 mL blood).
Used for: PCV by the Wintrobe method; largely historical, now replaced by EDTA in most laboratories.
Disadvantages: Distorts cell morphology on blood film, unsuitable for electrolyte/potassium estimation, and not used for coagulation tests.
9

## Slide 10
Heparin
Composition: A naturally occurring, sulfated mucopolysaccharide, extracted from animal (bovine/porcine) lung and intestinal mucosa.
Mechanism: Potentiates antithrombin III, which inactivates thrombin and Factor Xa directly — does NOT chelate calcium.
Ratio/Concentration: 0.1–0.2 mg (about 15–20 IU) per mL of blood (green-top vacutainer, lithium or sodium heparin).
Used for: Osmotic fragility test, blood gas analysis, ammonia estimation, chromosome studies/karyotyping, and tests requiring calcium to remain available.
Advantages: Physiological anticoagulant, rapid action, doesn't remove calcium — useful when calcium-dependent assays are needed.
Disadvantages: Expensive; causes leukocyte clumping; gives a bluish background on Romanowsky-stained films (unsuitable for blood film/differential count).
10

## Slide 11
Warfarin
An in vivo (therapeutic) anticoagulant — not used to preserve laboratory blood samples in vitro.
Mechanism: A Vitamin K antagonist — inhibits the hepatic synthesis of the Vitamin K-dependent clotting factors II, VII, IX, and X.
Use: Given orally to prevent and treat thromboembolic disorders — deep vein thrombosis, pulmonary embolism, atrial fibrillation, prosthetic heart valves.
Monitoring: Therapeutic effect is monitored using Prothrombin Time (PT), expressed as the International Normalized Ratio (INR).
Note: Included here as an anticoagulant classification, but relevant to pharmacology/clinical medicine rather than sample collection.
11

## Slide 12
Anticoagulants — Quick Comparison
Anticoagulant | Mechanism | Ratio / Conc. | Chief Use
EDTA | Chelates calcium | 1.2–2.0 mg/mL | CBC, blood film
Sodium Citrate | Chelates calcium (reversible) | 1:9 (PT/APTT); 1:4 (ESR) | Coagulation tests, ESR, blood bank
Double Oxalate | Precipitates calcium | ~6 mg/2 mL (3:2 ratio) | PCV (Wintrobe method)
Heparin | Inhibits thrombin/Factor Xa | 0.1–0.2 mg (15–20 IU)/mL | Osmotic fragility, blood gas, karyotyping
Warfarin | Vitamin K antagonist | Oral, dose-titrated (in vivo) | Therapeutic — thromboprophylaxis
12

## Slide 13
Anticoagulants in Blood Bank
Blood bank anticoagulants double as preservative solutions — they must keep donor blood both liquid AND viable for transfusion.
ACD (Acid Citrate Dextrose): Citrate chelates calcium; dextrose provides energy for RBC metabolism during storage. Shelf life ~21 days.
CPD (Citrate Phosphate Dextrose): Adds phosphate as a buffer to maintain pH and improve RBC survival. Shelf life ~21 days.
CPDA-1 (Citrate Phosphate Dextrose Adenine): Adenine allows RBCs to resynthesize ATP, extending shelf life to ~35 days.
SAGM (Saline-Adenine-Glucose-Mannitol): An additive solution used after plasma/citrate removal to extend red cell storage further (~42 days).
Choice of preservative determines shelf life, RBC viability, and suitability of the unit for specific transfusion needs.
13